## Slide 1: DSAGEN: Democratizing the Research on Spatial Accelerators
Jian Weng, Sihao Liu, Vidushi Dadu, Tony Nowatzki
University of California, Los Angeles
Oct. 17th, 2020

## Slide 2: Roadmap
Background: Decoupled Spatial Architectures
Hands-on Exercises
  Basics of Programming Decoupled-Spatial Architecture
    Example 1: Vector Add
      Hardware/Software Overview
      Hardware Simulation & Trouble Shooting
      Optimization: Unrolling Instructions
    Example 2: Vector Normalization
  Advanced DSA Programming
  Compiling High-Level Lang. to DSA
  Composing a Spatial Architecture
Notes: Thank you for introduction. In this section, I will introduce some basic principle of programming a decoupled-spatial architecture. I will first introduce the overview of hardware as well as the programming interface through vector addition. After implementation, I will also talk about the usage of simulator, including how to debug, read the log, and use the log to guide your optimization.
When you have something you do not follow, do be shy. Feel free to interrupt me.
Also, we made a lot of update to the example repo, so make sure you are up to date by typing git pull.

## Slide 3: Warm Up: Decoupled Spatial Execution
for (int i = 0; i < n; ++i)
c[i] = a[i] + b[i];
＋
a[0:n]
b[0:n]
c[0:n]
Controller
Memory
Mem. Controller
Memory
Sync. Elem
(Port)
Switches
Processing Elements
Address Generator
Ctrl Host
＋
b[0:n]
a[0:n]
c[0:n]
Notes: To program an accelerator with decoupled spatial execution, we should have a graph like this in your mind. First decouple the memory access and computational instructions and represent them in a data dependence graph so that they can be mapped to a spatial architecture.
A spatial architecture is composed by PEs for computations and switches for routing the dependences. In the figure on the rhs, red and purple circles are representing Pes with different features.
The decoupled memory access are encoded in control intrinsics issued from the control host to the memory controller. Then the memory controller sends memory request so that the data can stream through the spatial architecture to execute the program.
Sometimes, we want a proper timing of data arrival, so synchronization elements are injected before entering the spatial architecture, which are essentially coordination FIFO’s. In this case, the mapped graph will be triggered when both there are data available in a & b’s FIFO’s. In the rest of my talk, I will use the term port for these FIFO’s because it serves more on as an interface more than synchronization in our programming interface.

## Slide 4: Warm Up: Programming Interface
Controller
Memory
Mem. Controller
Memory
Sync. Elem
(Port)
Switches
Processing Elements
Address Generator
Ctrl Host
＋
B
A
C
Decoupled Memory: Memory Stream Intrinsics
  a[i,j] → a[i*stride+j]
  a[b[i]]
  Port-to-port comm.
Spatial Architecture: Data Dependence Graph w/ a Spatial Mapper
Sync. Elem
(Port)
a[0:n]
b[0:n]
c[0:n]
A
B
C
Notes: We have a decoupled execution model, so we also have a decoupled programming interface.
To program the spatial architecture, we need a representation for the data dependence graph for as well as a compiler that automatically maps this graph onto the spatial architecture.
To program the decoupled data access, we need hardware intrinsics to encode the data access with some specific patterns, like strided pointer and multi-level indirect access.
And these two are bridged by the ports mentioned before. Next, let’s first talk about how to program a spatial architecture, and expose the port the control host through a simple example.

## Slide 5: Software Interface: Dataflow Graph (manual/01_vector_add)
RISCV CPU
Memory
Mem. Controller
Rec Bus
(a) Data Dependence Graph
# Dataflow Graph
# compute.dfg
Input: A
Input: B C = Add64(A, B)
Output: C
(b) Data Dependence Graph (text format)
＋
B
A
C
＋
A
B
C
⌨ Edit compute.dfg
Notes: Let’s go to this directory in dsa-examples and open this file with your favorite editor.
Let’s type in these texts into this file.
When you are done, you can send an emoji to me.
Ideally, we want something to map this graph onto the spatial architecture and expose the ports A/B/C to us for programming the host.

## Slide 6: Software Interface: Dataflow Graph (CONT’D)
$SS/spatial.json
spatial-scheduler
$ make compute.dfg.h
$ ss_sched $SS/spatial.json compute.dfg
compute.dfg.h: the mapped sw/hw interf.
sched/*: mapped data in serialized form.
RISCV CPU
Memory
Mem. Controller
Rec Bus
# Dataflow Graph
# compute.dfg
Input: A
Input: B C = Add64(A, B)
Output: C
Data Dependence Graph (text format)
＋
B
A
C
Notes: To invoke the spatial compiler we need an abstraction to describe the spatial architecture, and here is the file, which will be discussed by my collaborator in the following sections.
This command will generate these files, and let’s open compute.dfg.h

## Slide 7: Warm Up: Dataflow Graph (CONT’D)
#ifndef __compute_H__ #define __compute_H__ #define P_compute_A 20 #define P_compute_B 10
#define P_compute_C 0 #define compute_size 96 char compute_config[96] = ...; #endif //compute_H
The number of ports to appear in the host control intrinsics.
The bitstream array.
This is for the simulation purpose.
SS_CONFIG(compute_config, compute_size); // Load bitstream
⌨ Edit main.cc
Notes: In this file, there are some macros.
P_compute_A/B/C are the number of the ports you are gonna plug in to memory access control intrinsics, and compute_* are parameters you are gonna plug into bitstream loading intrinsic.
So now, open the main.cc with me and write this intrinsic in the kernel function. Don’t be afraid, I already put comments as hints.

## Slide 8: Warm Up: Memory Intrinsics (dsaintrin.h)
RISCV CPU
Memory
Mem. Controller
Rec Bus
＋
B
A
C
// decoupled memory access
read a[0:n] → A
read b[0:n] → B
write C → c[0:n]
// vanilla code
for (int i = 0; i < n; ++i)
c[i] = a[i] + b[i];
a[0:n]
b[0:n]
A
B
C
c[0:n]
Notes: After configuration, here is the next question, how can we forward data to the spatial architecture?

## Slide 9: Warm Up: Memory Intrinsics (CONT’D)
addr[0:bytes] → port
  SS_LINEAR_READ(addr, bytes, port)
port → addr[0:bytes]
  SS_LINEAR_WRITE(port, addr, bytes)
SS_CONFIG(compute_config,
compute_size);
SS_LINEAR_READ(a, n*8, P_compute_A);
SS_LINEAR_READ(b, n*8, P_compute_B);
SS_LINEAR_WRITE(P_compute_C, b, n*8);
⌨ Append main.cc
// Pseudo-code for decoupled
// memory intrinsics
read a[0:n] → A
read b[0:n] → B
write C → c[0:n]
Notes: Remember to mention rectangle and triangle here.

## Slide 10: Memory Intrinsics: Barrier and Order!
SS_WAIT_ALL(): Stall the control host until all the streams are done.
All the memory streams before the barrier are concurrent (no order guaranteed).
Exception: Streams destinated the same port will be executed in order they appear.
SS_CONFIG(compute_config,
compute_size);
SS_LINEAR_READ(a, n*8, P_compute_A);
SS_LINEAR_READ(b, n*8, P_compute_B);
SS_LINEAR_WRITE(P_compute_C, n*8, b);
SS_WAIT_ALL();
⌨ Edit main.cc
// Pseudo-code for decoupled
// memory intrinsics
read a[0:n] → A
read b[0:n] → B
write C → c[0:n]
notify the host when accel. is done

## Slide 11: Example 1: Vector Add
SS_CONFIG(compute_config, compute_size);
SS_LINEAR_READ(a, 8*n, P_add_A);
SS_LINEAR_READ(b, 8*n, P_add_B);
SS_DMA_WRITE(P_add_C, c, 8*n);
SS_WAIT_ALL();
// vanilla code
for (int i = 0; i < n; ++i)
c[i] = a[i] + b[i];
＋
a[0:n]
b[0:n]
c[0:n]
RISCV CPU
Memory
Mem. Controller
Input: A
Input: B
C = Add64(A, B)
Output: C
// manual/compute.dfg.h
＋
b[0:n]
a[0:n]
c[0:n]
a[0:n]
b[0:n]
c[0:n]
🧠
$ make compute.dfg.h
$ ./run.sh main.out
⌨ Edit main.cc
⌨ Edit compute.dfg

## Slide 12: Example 1: Vector Add (Run it!)
$ ./run.sh main.out
Simulator Time: 0.02022 sec Cycles: 530 Number of coalesced SPU requests: 0 Control Core Insts Issued: 12 Control Core Discarded Insts Issued: 11 Control Core Discarded Inst Stalls: 0.9167 Control Core Config Stalls: 0.02642 Control Core Wait Stalls: 0.9755 (ALL) ACCEL 0 STATS *** Commands Issued: 3 CGRA Instances: 512 -- Activity Ratio: 0.966, DFGs / Cycle: 0.966 For backcgra, Average thoughput of all ports (overall): 0.966, CGRA outputs/cgra busy cycles: 1 CGRA Insts / Computation Instance: 1 CGRA Insts / Cycle: 0.966 (overall activity factor) Mapped DFG utilization: 0.966 Data availability ratio: 0 input port imbalance (%age dgra nodes could not fire): 0
// warm cache
kernel();
// profiling
begin_roi();
kernel();
end_roi();
sb_stats();

## Slide 13: Example 1: Vector Add (Unrolling/Vectorizing)
＋
＋
a[0:n]
b[0:n]
c[0:n]
＋
＋
# compute.dfg
Input: A[4]
Input: B[4]
C0 = Add64(A0, B0)
C1 = Add64(A1, B1)
C2 = Add64(A2, B2)
C3 = Add64(A3, B3)
Output: C[4]
// main.cc
SS_CONFIG(compute_config, compute_size);
SS_LINEAR_READ(a, 8*n, P_compute_A);
SS_LINEAR_READ(b, 8*n, n, P_compute_B);
SS_LINEAR_WRITE(PC, 8*n, P_compute_C);
SS_WAIT_ALL();
⌨ Edit main.cc
⌨ Edit compute.dfg
Explore the resource occupation on the spatial architecture.
＋
a[0:n]
b[0:n]
c[0:n]

## Slide 14: Example 1: Vector Add (Run it!)
*** ROI STATISTICS for CORE ID: 0 *** Simulator Time: 0.01516 sec Cycles: 148 Number of coalesced SPU requests: 0 Control Core Insts Issued: 12 Control Core Discarded Insts Issued: 11 Control Core Discarded Inst Stalls: 0.9167 Control Core Config Stalls: 0.09459 Control Core Wait Stalls: 0.9122 (ALL)
ACCEL 0 STATS *** Commands Issued: 3 CGRA Instances: 128 -- Activity Ratio: 0.8649, DFGs / Cycle: 3.459
For backcgra, Average thoughput of all ports (overall): 0.8649, CGRA outputs/cgra busy cycles: 1 CGRA Insts / Computation Instance: 4 CGRA Insts / Cycle: 3.459 (overall activity factor)

## Slide 15: Trouble Shooting: Unbalanced Streams!
// main.cc
SS_CONFIG(add_config, add_size);
SS_LINEAR_READ(a, 8*n, P_add_A);
// SS_LINEAR_READ(b, 8*n, P_add_B);
SS_DMA_WRITE(P_add_C, c, 8*n);
SS_WAIT_ALL(); // forever spin
RISCV CPU
Memory
Mem. Controller
Rec Bus
＋
B
A
C
$ ./run.sh main.out

## Slide 16: Trouble Shooting (CONT’D)
Active SEs: dma->port dim[0]: stride=0, trip_cnt=0/1, stretch=0 innermost: current=81856, acc_size=568/4096 in_port=1(A) repeat_in=1 stretch=0 ACTIVE port->dma dim[0]: stride=0, trip_cnt=0/1, stretch=0 innermost: current=73096, acc_size=0/4096 out_port=0(C) garbage=0 ACTIVE Waiting SEs: (0) Non-empty buffers: Ports: In Port 1 A: Mem Size: 3 Num Ready: 8 Rem writes: 0 In Port 0 B: Mem Size: 0 Num Ready: 0 Rem writes: 0 Ind In Port 23: Mem Size: 0 Num Ready: 0 Rem writes: 0 Ind In Port 24: Mem Size: 0 Num Ready: 0 Rem writes: 0 Ind In Port 25: Mem Size: 0 Num Ready: 0 Rem writes: 0 Ind In Port 26: Mem Size: 0 Num Ready: 0 Rem writes: 0 Ind In Port 27: Mem Size: 0 Num Ready: 0 Rem writes: 0 Ind In Port 28: Mem Size: 0 Num Ready: 0 Rem writes: 0 Ind In Port 29: Mem Size: 0 Num Ready: 0 Rem writes: 0 Ind In Port 30: Mem Size: 0 Num Ready: 0 Rem writes: 0 Ind In Port 31: Mem Size: 0 Num Ready: 0 Rem writes: 0 Out Port 0 C: In Flight: 0 Num Ready: 0 Mem Size: 0

## Slide 17: Roadmap
Background: Decoupled Spatial Architectures
Hands-on Exercises
  Basics of Decoupled-Spatial Architecture Infra
    Example 1: Vector Add
    Example 2: Vector Normalization
      Predicated Accumulator
      Multi-DFG Graph
      Programmable Ports
  Advanced DSA Programming
  Compiling High-Level Lang. to DSA
  Composing a Spatial Architecture

## Slide 18: Example 2: Vector Normalization (manual/02_vector_norm)
double norm = 0.0; for (int i = 0; i < n; ++i) norm += a[i] * a[i]; norm = 1.0 / sqrt(norm); for (int i = 0; i < n; ++i) a[i] = a[i] * norm;
❷
❶
❶ norm is finalized after n times accumulation.
❸
×
＋
√
×
/

## Slide 19: New Feature: Signaled Accumulator
Input: A
Input: B
C = FMul64(A, A)
O = FAdd64(B, C)
Output: O
double norm = 0.0; for (int i = 0; i < n; ++i) norm += a[i] * a[i];
Input: A
Input: S
TMP = FMul64(A, A)
O = FAccumulate64(
TMP, ctrl=S{0:r,1:d})
Output: O
FAccumulate64(B)
  Accumulate B to the local register
ctrl=signal{a:b}: The control predicate.
  d: discard the produced value
  r: reset the registers to 0

## Slide 20
SS_CONST(port, value, n_times)
  Forward constant value n_times to the given port
Input: A
Input: S
TMP = FMul64(A, A)
O = FAccumulate64(
TMP, ctrl=S{0:r, 1:d})
Output: O
SS_CONFIG(compute_config, compute_size);
SS_LINEAR_READ(a, n*8, P_compute_A);
SS_CONST(P_compute_S, 1, n-1);
SS_CONST(P_compute_S, 0, 1);
⌨ Edit main.cc
New Feature: Signaled Accumulator
⌨ Edit compute.dfg

## Slide 21: Example 2: Vector Normalization
double norm = 0.0; for (int i = 0; i < n; ++i) norm += a[i] * a[i]; norm = 1.0 / sqrt(norm); for (int i = 0; i < n; ++i) a[i] = a[i] * norm;
❷
❶
❷ finalized norm is consumed by a scalar inverse operation.
❸
×
＋
√
×
/

## Slide 22: New Feature: Temporally Shared PE
RISCV CPU
Memory
Mem. Controller
Rec Bus
norm = 1.0 / sqrt(norm);
...
----
#pragma group temporal
Input: NORM2
NORM = Sqrt(NORM2)
INV = FDiv64(1.0, NORM2)
Output: INV
⌨ Append compute.dfg
×
＋
A
O
NORM2
√
INV
S
/

## Slide 23: New Feature: Port-to-Port Communication
# compute.dfg
Input: A
Input: S
TMP = FMul64(A, A)
O = FAccumulate64(TMP,
ctrl=S{1:d})
Output: O
----
#pragma group temporal
Input: NORM2
NORM = Sqrt(NORM2)
INV = FDiv(1.0, NORM2)
Output: INV
----
Input: V
Input: C
B = FMul64(V, C)
Output: B
double norm = 0.0; for (int i = 0; i < n; ++i) norm += a[i] * a[i]; norm = 1.0 / sqrt(norm); for (int i = 0; i < n; ++i) a[i] = a[i] * norm;
SS_WAIT_ALL();
SS_CONST(P_NORM2,
/*Result from Port O*/);
⌨ Append main.cc

## Slide 24: New Feature: Port-to-Port Communication
RISCV CPU
Memory
Mem. Controller
Rec Bus
×
＋
A
O
NORM2
√
INV
×
V
C
B
S
/
SS_RECURRENCE(o_port, i_port, n)
  Forward n values produced by o_port to the i_port
SS_LINEAR_READ(P_compute_A, a, n * 8);
SS_CONST(P_compute_B, 1, n-1);
SS_CONST(P_compute_B, 0, 1);
SS_RECURRENCE(P_compute_O, P_compute_NORM2, 1);
SS_RECURRENCE(P_compute_INV, P_compute_C, 1);
⌨ Append main.cc

## Slide 25: Example 2: Vector Normalization
double norm = 0.0; for (int i = 0; i < n; ++i) norm += a[i] * a[i]; norm = 1.0 / sqrt(norm); for (int i = 0; i < n; ++i) a[i] = a[i] * norm;
❷
❶
❸ the produce norm is reused n times.
❸
×
＋
√
×
/

## Slide 26: New Features: Programmable FIFO
SS_REPEAT_PORT(N)
  Set the repeat register.
  Each element in the next instantiated stream will be repeated N times.
  Will be automatically reset to 1 after stream instantiation.
Stream: 1, 2, 3, 4, ...
Stream (Repeat by 4): 1, 1, 1, 1, 2, 2, 2, 2, 3, 3, 3, 3, ...
SS_RECURRENCE(P_compute_O, P_compute_NORM2, 1);
SS_REPEAT_PORT(N);
SS_RECURRENCE(P_compute_INV, P_compute_C, 1);

## Slide 27
Example 2: Vector Normalization
// compute.dfg
Input: A
Input: S
TMP = FMul64(A, A)
O = FAccumulate64(TMP,
ctrl=S{1:d})
Output: O
----
#pragma group temporal
Input: NORM2
NORM = Sqrt64(NORM2)
INV = FDiv(1.0, NORM)
Output: INV
----
Input: V
Input: C
B = FMul64(V, C)
Output: B
// main.cc
SS_CONFIG(compute_config, compute_size);
SS_LINEAR_READ(a, 8 * N, P_compute_A);
SS_CONST(P_compute_S, 1, N–1);
SS_CONST(P_compute_S, 0, 1);
SS_RECURRENCE(P_compute_O, P_compute_NORM2, 1);
SS_REPEAT_PORT(N);
SS_RECURRENCE(P_compute_INV, P_compute_C, 1);
SS_LINEAR_READ(a, 8*N, P_compute_V);
SS_LINEAR_WRITE(P_compute_B, a, 8*N);
SS_WAIT_ALL();
⌨ Edit main.cc

## Slide 28: $ ./run.sh main.out
Simulator Time: 0.01722 sec Cycles: 274 Number of coalesced SPU requests: 0 Control Core Insts Issued: 17 Control Core Discarded Insts Issued: 11 Control Core Discarded Inst Stalls: 0.6471 Control Core Config Stalls: 0.05109 Control Core Wait Stalls: 0.9526 (ALL) ACCEL 0 STATS *** Commands Issued: 7 CGRA Instances: 130 -- Activity Ratio: 0.938, DFGs / Cycle: 0.4745 For backcgra, Average thoughput of all ports (overall): 0.1582, CGRA outputs/cgra busy cycles: 0.5 058 CGRA Insts / Computation Instance: 2.969 CGRA Insts / Cycle: 1.409 (overall activity factor)

## Slide 29: 5-Minute Break

## Slide 30: Roadmap
Background: Decoupled Spatial Architectures
Hands-on Exercises
  Basics of Decoupled-Spatial Architecture Infra
  Advanced DSA Programming
  Compiling High-Level Lang. to DSA
    Pragma Annotated Compilation
      Why pragma’s?
    Example 1: Vector Add
    Modular Compilation with Examples
  Composing a Spatial Architecture

## Slide 31: Compiling High-Level Lang. to Decoupled Spatial
Programmer Hints
  Which code regions are offloaded onto the spatial accelerator?
  Which memory accesses can be decoupled intrinsics?
  Which offloaded regions should be concurrent?
Executable Binary
Apps
?
How to abstract diverse underlying features with a unified high-level interface?
Pragma Annotation
Notes: We have a wide design space, so our programming language needs to be generic enough. This means a DSL, like Halide or TF, does not suffice.
Instead we adopt C.
The key challenge to overcome is how to have a unified high-level interface to abstract the diverse underlying hardware.
In order to do this without massive compiler effort, we rely on programmers to provide these hints.

## Slide 32: Roadmap
Background: Decoupled Spatial Architectures
Hands-on Exercises
  Basics of Decoupled-Spatial Architecture Infra
  Advanced DSA Programming
  Compiling High-Level Lang. to DSA
    Pragma Annotated Compilation
    Example 1: Vector Add
      An exemplified pragma’s annotation!
    Modular Compilation with Examples
  Composing a Spatial Architecture

## Slide 33: Pragmas --- Which to Offload?
#pragma ss dfg [temporal] [unroll(x)]
  Annotate either a loop or a compound body
  Enable temporal if you want to offload onto shared Pes
  Enable unroll if you want to occupy more FU resources
// vanilla code
for (int i = 0; i < n; ++i)
c[i] = a[i] + b[i];
#pragma ss dfg unroll(4)
for (int i = 0; i < n; ++i)
c[i] = a[i] + b[i];

## Slide 34: Pragmas --- What to Decouple?
#pragma ss stream [nonblock]
  Annotate a loop
  Hints that the memory access below are restrict
  Enable the clause if you do not want to inject SS_WAIT_ALL to sync after this region is done
#pragma ss stream
#pragma ss dfg unroll(4)
for (int i = 0; i < n; ++i)
c[i] = a[i] + b[i];
#pragma ss dfg unroll(4)
for (int i = 0; i < n; ++i)
c[i] = a[i] + b[i];

## Slide 35: Pragmas --- What to be concurrent?
#pragma ss config
  Annotate a compound body
  The #pragma ss dfg in this body will be concurrent on the spatial architecture
#pragma ss stream
#pragma ss dfg unroll(4)
for (int i = 0; i < n; ++i)
c[i] = a[i] + b[i];
#pragma config
{
#pragma ss stream
#pragma ss dfg unroll(4)
for (int i = 0; i < n; ++i)
c[i] = a[i] + b[i];
}

## Slide 36: Example 1: Vector Add (Pragma Compilation)
// compile/main.cc
#pragma config
{
#pragma ss stream
#pragma ss dfg unroll(4)
for (int i = 0; i < n; ++i)
c[i] = a[i] + b[i];
}
Modified clang
main.bc
DSA Xform Pass
dsa-main.bc
DFG’s
Generic Opt.
O3-dsa-main.bc
Code Select
O3-dsa-main.s
GNU Linker
O3-dsa-main.out
$ ./run.sh O3-dsa-main.out
$ ./run.sh main.out
Notes: To program an accelerator with such programming paradigm, we need to decouple the computation and memory accesses in order to map them to the corresponding hardware component.
The computations are represented in a data dependence graph and mapped onto a spatial architecture which consist of PEs for performing computations and switches for routing the dependences.
The memory access are encoded in control intrinsics issued from the control host to the memory controller. Then the memory controller sends memory request so that the data can stream through the spatial architecture to execute the program.
When multiple data streams need to be synchronized, a sync. elem. made of coordinating FIFOs will ensure a proper timing.
I will discuss the design tradeoffs of the key hardware primitives in the next a few slides.

## Slide 37: Decoupled-Spatial Xform
// compile/main.cc
#pragma config
{
#pragma ss stream
#pragma ss dfg unroll(4)
for (int i = 0; i < n; ++i)
c[i] = a[i] + b[i];
}
# compile/main.bc
%0 = call ss.config.begin()
i = 0
loop:
%1 = load a[i]
%2 = load b[i]
%3 = add %1, %2
store c[i], %2
i += 1
br i < n, loop !0
%4 = call ss.config.end(%0)
!0 = {"ss.dfg", 4, !1}
!1 = {"ss.stream"}
❶
❷
⓿ Config scopes are guarded by intrinsic functions
❶ Loop hints are encoded in metadata
❷ Starting with memory loads and ending with memory store, traverse the dependence graph to decouple them. Memory instructions will be analyzed and encoded in control cmd.
❸ Decoupled computational instructions are duplicated by the unrolling degree and fed to the spatial compiler.
❸
⓿
Clang Compiler

## Slide 38: Decoupled-Spatial Xform
# compile/main.bc
%0 = call ss.config.begin()
i = 0
loop:
%1 = load a[i]
%2 = load b[i]
%3 = add %1, %2
store c[i], %2
i += 1
br i < n, loop !0
%4 = call ss.config.end(%0)
!0 = {"ss.dfg", 4, !1}
!1 = {"ss.stream"}
Input: sub0_1[4]
Input: sub0_2[4]
sub0_30 = Add64(sub0_10, sub0_20)
sub0_31 = Add64(sub0_11, sub0_21)
sub0_32 = Add64(sub0_12, sub0_22)
sub0_33 = Add64(sub0_13, sub0_23)
Output: sub0_3[4]
SS_CONFIG(X_config, X_size)
SS_LINEAR_READ(a, 8*n, P_X_sub0_1)
SS_LINEAR_READ(b, 8*n, P_X_sub0_2)
SS_LINEAR_WRITE(P_X_sub0_3, a, 8*n)
i = 0
loop:
i += 1
br i<n, loop !0
SS_WAIT_ALL()
!0 = {"ss.dfg", 4, !1}
!1 = {"ss.stream"}
This loop will be eliminated when generic optimization

## Slide 39: Example 2: Vector Normalization (Compilation)
acc = 0.0; for (int i = 0; i < N; ++i) acc += a[i] * a[i]; norm = 1.0 / sqrt(acc); for (int i = 0; i < N; ++i) a[i] = a[i] * norm;
acc = 0.0;
#pragma ss stream
#pragma ss dfg for (int i = 0; i < N; ++i) acc += a[i] * a[i];

## Slide 40: Example 2: Vector Normalization (CONT’D)
acc = 0.0; for (int i = 0; i < N; ++i) acc += a[i] * a[i]; norm = 1.0 / sqrt(acc); for (int i = 0; i < N; ++i) a[i] = a[i] * norm;
acc = 0.0;
#pragma ss stream nonblock
#pragma ss dfg for (int i = 0; i < N; ++i) acc += a[i] * a[i];
#pragma ss dfg temporal
{ norm = 1.0 / sqrt(acc);
}
nonblock: Since the result of the accumulation region is forward to the scalar region, we do not want to sync the first region.

## Slide 41: Example 2: Vector Normalization (CONT’D)
acc = 0.0; for (int i = 0; i < N; ++i) acc += a[i] * a[i]; norm = 1.0 / sqrt(norm); for (int i = 0; i < N; ++i) a[i] = a[i] * norm;
double acc = 0.0;
#pragma ss stream nonblock
#pragma ss dfg for (int i = 0; i < N; ++i) acc += a[i] * a[i];
#pragma ss dfg temporal
{ norm = 1.0 / sqrt(acc);
}
#pragma ss stream
#pragma ss dfg for (int i = 0; i < N; ++i) a[i] = a[i] * norm;

## Slide 42: Example 2: Vector Normalization (CONT’D)
acc = 0.0; for (int i = 0; i < N; ++i) acc += a[i] * a[i]; norm = 1.0 / sqrt(norm); for (int i = 0; i < N; ++i) a[i] = a[i] * norm;
#pragma ss config
{
double acc = 0.0;
#pragma ss stream nonblock
#pragma ss dfg for (int i = 0; i < N; ++i) acc += a[i] * a[i];
#pragma ss dfg temporal
{ norm = 1.0 / sqrt(acc);
}
#pragma ss stream
#pragma ss dfg for (int i = 0; i < N; ++i) a[i] = a[i] * norm;
}

## Slide 43: ./run.sh O3-dsa-main.out
Simulator Time: 0.01652 sec Cycles: 275 Number of coalesced SPU requests: 0 Control Core Insts Issued: 38 Control Core Discarded Insts Issued: 27 Control Core Discarded Inst Stalls: 0.7105 Control Core Config Stalls: 0.05091 Control Core Wait Stalls: 0.9127 (ALL) ACCEL 0 STATS *** Commands Issued: 6 CGRA Instances: 130 -- Activity Ratio: 0.9382, DFGs / Cycle: 0.4727 For backcgra, Average thoughput of all ports (overall): 0.1576, CGRA outputs/cgra busy cycles: 0.5 039 CGRA Insts / Computation Instance: 2.969

## Slide 44: Modular Compilation
By default, the compiler assumes all the features are enabled.
When disabled, a fallback transformation escapes this feature is invoked.
  TEMPORAL Processing Elements --- 02_vector_norm
  RECcurrence Bus --- 03_gemm.cc
  INDirect Memory --- 04_crs.cc
Use these bold words environment variable to 0 to disable the corresponding feature and try the workloads.

## Slide 45: TEMPORAL=0 ./run.sh O3-dsa-main.out
Simulator Time: 0.02559 sec Cycles: 1691 Number of coalesced SPU requests: 0 Control Core Insts Issued: 880 Control Core Discarded Insts Issued: 115 Control Core Discarded Inst Stalls: 0.1307 Control Core Config Stalls: 0.008279 Control Core Wait Stalls: 0.07629 (ALL) ACCEL 0 STATS *** Commands Issued: 5 CGRA Instances: 129 -- Activity Ratio: 0.152, DFGs / Cycle: 0.07629 For backcgra, Average thoughput of all ports (overall): 0.03814, CGRA outputs/cgra busy cycles: 0. 5019 CGRA Insts / Computation Instance: 2.977 CGRA Insts / Cycle: 0.2271 (overall activity factor)

## Slide 46: Roadmap
Background: Decoupled Spatial Architectures
Hands-on Exercises
  Decoupled-Spatial Architecture Programming
  Advanced DSA Programming
  Composing a Spatial Architecture
  DSAGEN for your Research
    Adding a New Instruction Capability to Processing Elements
      Overview: The Organization of Spatial Schedule
      Integrate the Instruction
    Adding a New Host Control Command

## Slide 47: Our Goal: Adding an Instruction Capability to Spatial Processing Elements
Mixed precision instruction is a newly emerging idiom in many general-purpose processors
Give our spatial PEs the capability of this instruction
// ARM SDOT.i8.v64
int32_t c[2];
int8_t a[8], b[8];
for (i=0; i<2; ++i) {
for (j=0; j<4; ++j) {
int32_t A = (int32_t)a[i*4+j];
int32_t B = (int32_t)b[i*4+j];
c[i] += A * B;
}
}

## Slide 48: A Brief Codebase Walk Through (Spatial Scheduler)
src/arch/*: Data structures for hardware description.
src/dfg/*: Data structures for parsed dataflow graph.
Dataflow graph simulation.
src/mapper/*: Strategies for adjusting the spatial mapping.
src/schedule/*: Data structures that records spatial mapping
src/insts/*: Instruction enum, information (II, lat, power, area, and etc.), and behavior simulation.
drivers/*: The drivers of scheduler and design space explorer.
Automatically generate
  The registered instruction enum
  Integrate the instruction behavior for simulation
  Helper functions getting the information

## Slide 49: Add a New PE Instruction
src/insts/inst_model.cpp: the implementation of an instruction integration generator, which generates:
  The enum of each instruction.
  A function that dispatches enum to simulation behaviors.
  Helper functions that returns the information of each instruction:
    II, name, latency, and num of operands/outputs
./inst_model [index of instructions] [power/area] [output header] [output cxx]
  Index of Instructions: ssinst.full
  Power/area information gathered from synthesis
  Output Header/CXX: The name of the output files.

## Slide 50: What instructions are available on the spatial accelerator?
src/insts/full.ssinst: The metadata of each instruction.
How do I extend my instructions?
#Instruction Bitwidth NumOperands OutputValues Latency II
Add64 64 2 1 2 1
src/insts/inst_model.cpp: The instruction metadata generator.
./inst_model [index of instructions] [power/area] [output header] [output cxx]
  Use src/insts/full.ssinst as index to gather affiliated metadata of each instruction, including power, area, and simulation behavior.
// Return the first output
uint64_t execute(
std::vector<uint64_t> &ops, // Operands
std::vector<uint64_t> &outs, // Other outputs
std::vector<uint64_t> &regs, // Register File
std::vector<uint64_t> &discard, // Data Predicate
std::vector<uint64_t> &back_array // Backpressure
) {
return (int64_t) ops[0] + (int64_t) ops[1];
}

## Slide 51: Add a New PE Instruction (Cleanup)
Be careful about the data type casting!
It is something like “soft-float” ABI — uint64_t is actually storing the binary format of a floating-point number.
double a = (double) ops[0];
double b = (double) ops[1];
return (uint64_t) a * b;
double a = *reinterpret_cast<double*>(&ops[0]);
double b = *reinterpret_cast<double*>(&ops[1]);
double c = a * b;
return *reinterpret_cast<double*>(&c);

## Slide 52: Roadmap
Background: Decoupled Spatial Architectures
Hands-on Exercises
  Decoupled-Spatial Architecture Programming
  Advanced DSA Programming
  Composing a Spatial Architecture
  DSAGEN for your Research
    Adding a New Instruction Capability to Processing Elements
    Adding a New Host Control Command
      Overview: The sw/hw Interface and Hardware Simulator
      Adding the Instruction along with the Code Path

## Slide 53: What if we do not want to accumulate from zero?
Proposed Solution: Add a control command to modify the register file of PEs.
Software Interface:
  SS_SET_REG(inst, reg_id, value)
  Set the reg_idth register of PE to which the instruction is mapped to value.
Implement the interface:
  Binary Assembler
  Hardware Simulator
// manual/compute.dfg
Input: A
Input: S
B = FMul64(A, A)
O = FAccumulate64(B,
ctrl=S{1:d})
Output: O
----
#pragma group temporal
Input: NORM2
NORM = Sqrt(NORM2)
INV = FDiv(1.0, NORM2)
Output: INV
----
Input: V
Input: C
B = FMul64(V, C)
Output: B
ID
00
01
02
03
04
05
06
07
08
09
10
11
12

## Slide 54: Our Goal: Adding a Control Command
Change the register file in a specific PE
  It is useful when accumulating from a non-zero initial value.
Software/hardware interface:
  #define SS_REG_WRITE(inst_id, reg_id, value) \
  ss_reg_set $rs1, $rs2, imm
  Change the value of the register whose subscript is reg_id in PE to which instruction whose ID is inst_id is mapped to value.
Compiler
  Binary format, and mnemonic
Hardware Simulator
  Decode and dispatch to the accelerator
// manual/compute.dfg
Input: A
Input: S
B = FMul64(A, A)
O = FAcc64(B, S)
Output: O
----
#pragma group temporal
Input: NORM2
NORM = Sqrt(NORM2)
INV = FDiv(1.0, NORM2)
Output: INV
----
Input: V
Input: C
B = FMul64(V, C)
Output: B
id
00
01
02
03
04
05
06
07
08
09
10
11
12

## Slide 55: A Brief Codebase Walk Through (Hw/Sw Interf. & Sim.)
dsa-riscv-ext
riscv-gnu-toolchain
dsa-gem5
spatial-scheduler
dsa-binary
programs
dsa-llvm-project
arch/arch/riscv/decode.isa
src/cpu/minor/exec_context.h
src/cpu/minor/ssim/*
opcodes-dsa
riscv-dsa.c
autopatch.py
dsaintrin.h
binary format of the extended ISA
mnemonic of the extended ISA
macro intrinsic wrapper
Patch the binary assembler and of GNU toolchain.
Decode the instruction
Execute the instruction
Change the data structure of the spatial accelerator
Infra Build
Workload Compilation
Runtime Simulation

## Slide 56: Dive into the Extended ISA: Custom Slots of RISCV
#define SS_DMA_READ(addr, stride, size, n, port) \
__asm__ __volatile__("ss_dma_rd %1, %2, %3", "r"(stride), "r"(n), "i"(1)) \
__asm__ __volatile__(“ss_dma_rd %1, %2, %3”, “r”(addr), “r”(size), "i"((port)<<1))
opcode Inst[4:2] | opcode Inst[6:5] | funct3 |  |  |  |  |  |  | 
 |  | 0 | 1 | 2 | 3 | 4 | 5 | 6 | 7
010 | 00 | cfg_port | ctx | cfg | fill_mode |  |  |  | 
010 | 01 | add_port | scr_rd | seg_reg | dma_rd | const | recv | atom_op | cfg_mmap
110 | 10 |  | wr_scr | rem_port | wr_dma | grab | wr_rd | const_scr | cfg_atopm_op
110 | 11 | stride |  | set_iter | wait_df | wait | ind | ind_wr | cfg_ind
#define SS_SET_REG(id, reg, value) \
__asm__ __volatile__("ss_set_reg %1, %2, %3", "r"(id), "r"(value), "i"(reg))

## Slide 57: A Brief Codebase Walk Through (Hw/Sw Interf. & Sim.)
dsa-riscv-ext
riscv-gnu-toolchain
dsa-binary
programs
dsa-llvm-project
opcodes-dsa
riscv-dsa.c
autopatch.py
dsaintrin.h
binary format of the extended ISA
mnemonic of the extended ISA
macro intrinsic wrapper
Infra Build
#mnemonic operands functc3 i[6:5] i[4:2] i[1:0] ss_dma_rd rs1 rs2 bimm12hi bimm12lo 14..12=3 6..5=1 4..2=2 1..0=3 # S-type
ss_set_reg rs1 rs2 bimm12hi bimm12lo 14..12=2 6..5=1 4..2=2 1..0=3 # S-type
{"ss_dma_rd", 0, INSN_CLASS_I, "s,t,q", MATCH_SS_DMA_RD, MASK_SS_DMA_RD, match_opcode, 0},
{"ss_seg_reg",0, INSN_CLASS_I, "s,t,q", MATCH_SS_DMA_RD, MASK_SS_DMA_RD, match_opcode, 0},
dsa-riscv-ext/opcodes-dsa
Binary Compilation
Patched bin-utils
dsa-riscv-ext/riscv-dsa.c
$ make dsa-riscv-ext

## Slide 58: A Brief Codebase Walk Through (Simulation)
dsa-gem5/src/cpu/minor/ssim/accel.cc
RISCV CPU
Memory
Mem. Controller
dss-gem5/src/arch/riscv/isa/decoder.isa
dsa-gem5/src/cpu/minor/exec_context.hh
dsa-gem5/src/cpu/minor/ssim/ssim.cc
spatial-scheduler/src/dfg/ssdfg.cpp
Rec Bus
Execute the streams and coordinate the interface FIFO buffer.
Execute the dataflow graph with the delay and latency information.
// dsa-gem5/src/arch/riscv/isa/decode.isa
0xa: decode FUNCT3 { // 0xa = 10 = 2^4+2
// ...
0x2: SSOp::ss_dma_rd({{ xc->pushStreamDimension(Rs1, Rs2, imm >> 1); if (~imm & 1) { xc->callSSFunc(SS_MEM_PRT);
} }}, IsSSStream, IsNonSpeculative, No_OpClass);
0x3: SSOp::ss_set_reg({{
// Pass Rs1, Rs2, Rs3 to xc state xc->callSSFunc(SS_SET_REG);
}}, IsSSStream, IsNonSpeculative, No_OpClass);
// dsa-gem5/src/cpu/minor/ isa/exec_context.hh
switch(ss_func_code) {
// ...
case SS_PRT_MEM: ssim.write_dma(); break;
case SS_SET_REG:
ssim.accel->sched->dfg->nodes[id]
->_reg[idx] = val;
break;

## Slide 59: Resources
Tutorial Website
  http://www.seas.ucla.edu/~jianw/dsagen/tutorial.html
Released Source
  https://github.com/PolyArch/dsa-framework
Binary and Docker
  On Tutorial Website
Hands-on Exercises
  https://github.com/PolyArch/dsa-examples
Related Papers
  Jian Weng=, Sihao Liu=, Vidushi Dadu, Zhengrong Wang, Tony Nowatzki, “DSAGEN: Synthesizing Programmable Spatial Architectures”, ISCA 2020
  Jian Weng, Sihao Liu, Zhengrong Wang, Vudushi Dadu, Tony Nowatzki, “A Hybrid Systolic-Dataflow Architecture for Inductive Matrix Algorithms”, HPCA 2020
  Vidushi Dadu, Jian Weng, Sihao Liu, Tony Nowatzki, “Toward General Purpose Acceleration by Exploiting Common Data-Dependence Forms”, MICRO 2019