## Slide 1: Outline
Background: Decoupled Spatial Architectures​
Decoupled-Spatial Architecture Programming​
Advanced DSA Programming​
  Warm up: Support for data-dependent control/memory
  Exercise 3: Sparse vector-vector dot-product (Hands-on-exercise)
  Full SpMSpV with Multi-core implementation
Compiling High-Level Lang. to DSA​
Composing a Spatial Architecture​

## Slide 2: Outline
Background: Decoupled Spatial Architectures​
Decoupled-Spatial Architecture Programming​
Advanced DSA Programming​
  Warm up: Support for data-dependent control/memory
  Exercise 3: Sparse vector-vector dot-product (Hands-on-exercise)
  Full SpMSpV with Multi-core implementation
Compiling High-Level Lang. to DSA​
Composing a Spatial Architecture​

## Slide 3: Challenges with Irregular Workloads: SpMSpV Example
1 | 0 | 4 | 1 | 0 | 0 | 0
2 | 0 | 0 | 0 | 7 | 0 | 0
0 | 0 | 0 | 0 | 0 | 0 | 9
0 | 3 | 3 | 1 | 1 | 0 | 0
0 | 2 | 0 | 0 | 0 | 0 | 3
2 | 0 | 5 | 0 | 0 | 0 | 0
0 | 0 | 0 | 0 | 0 | 0 | 0
1 | 0 | 0 | 0 | 6 | 0 | 0
2 | 3 | 4 | 0 | 0 | 0 | 0
0 | 2 | 0 | 3 | 0 | 4 | 0
3
0
0
9
4
0
0
0
6
Input Vector A (N)
Output Vector C (N)
×
∑
Input Matrix B (NxN)
2 | 3 | 4
idx
1 | 3 | 5
val
A
B[0]
0 | 2 | 3
1 | 4 | 1
idx
val
Dot product in CSR format
total+=3*1
Output of conditional
Conditional output 0 means no multiplication
0
0
0
1
0
Notes: // join of indices SS_DMA_READ(&matrix_row_ind[row_offset[row]], 0, (row_offset[row+1]-row_offset[row]) * 8, 1, P_dotp_indA); SS_CONST(P_dotp_indA, sentinel, 1); SS_DMA_READ(&vector_ind[0], 0, vec_len * 8, 1, P_dotp_indB); SS_CONST(P_dotp_indB, sentinel, 1); // indirect access to the values of matched indices (unknown length) SS_INDIRECT(P_dotp_matchIndA, &matrix_row_val[row_offset[row]], M, P_dotp_matchValA); SS_INDIRECT(P_dotp_matchIndB, &vector_val[0], M, P_dotp_matchValB); // reset all streams when the output is accumulated SS_RECV(P_dotp_O, output[row]); SS_RESET(); SS_WAIT_ALL();

## Slide 4
// vanilla C code
while (i < an && j < bn):
if (indA[i] == indB[j]):
matchInd[++iout] = indA
++i; ++j
elif (indA < indB):
++i
else:
++j
<
f
indB [nextIdxB]
indA [nextIdxA]
matchedInd[0:N]
0
=
Dot Product Implementation with Existing Features
Sel
Sel
+
+
nextIdxA
nextIdxB
1. Indirect memory access
2. Unknown #matches
pred
indB
indA

## Slide 5: Feature 1: Data-dependent memory access
Semantics: a[b[i]]
SS_INDIRECT(ind_port, addr, num_elem, input_port);
for data in ind_port:
calc_addr = addr + data
send data to input_port
Stream-dataflow intrinsic
2 | 7 | 3 | 4
a[0] | a[1] | a[2] | a[3] | a[4] | a[5] | a[6] | a[7]
b[0:4]
Notes: Specify the parent stream from “parent_port”
New address is calculated using addr_offset + (b[i]:data at parent_port)
Write the stream to input_port

## Slide 6: Feature 2: Data-dependent length
SS_RECV(port, mem_addr)
Port A
mem_addr
Acts as a barrier until a value from a port is written to a memory location
SS_RESET()
Resets all pending read requests and active streams except live data
Notes: SS_RESET()
for existing read streams: drops pending requests and sets num_elem to 0
For existing write streams: sets num_elem to 0 when the vector_port is empty
/*! * \brief Drop all the ongoing data request while retaining the configuration. */#define SS_RESET() \ __asm__ __volatile__("ss_cfg x0, 0") /*! * \brief Reset all live streams after finishing all ports */#define SS_STREAM_RESET() \ __asm__ __volatile__("ss_cfg x0, 1");

## Slide 7: Dot product Impl. Using Indirect Access (manual/ 04_bad_join with N=4096, DENSITY=0.1)
Simulator Time: 0.05903 sec
Cycles: 1798
Number of coalesced SPU requests: 0
Control Core Insts Issued: 37
Control Core Discarded Insts Issued: 17
Control Core Discarded Inst Stalls: 0.4595
Control Core Config Stalls: 0.07731
Control Core Wait Stalls:
ACCEL 0 STATS ***
Commands Issued: 5
CGRA Instances: 868 -- Activity Ratio: 0.2286, DFGs / Cycle: 0.4828
For backcgra, Average thoughput of all ports (overall): 0.1207, CGRA outputs/cgra busy cycles: 2.112
CGRA Insts / Computation Instance: 4.368
CGRA Insts / Cycle: 2.108 (overall activity factor)
Mapped DFG utilization: 0.1917
Low activity ratio
Why?

## Slide 8: Cyclic Dependence Loop Limits the Throughput However Unnecessary
Recv (out)
<
m
indB [nextIdxB]
indA [nextIdxA]
matchedInd[0:N]
Reset
0
=
=
Sel
Sel
+
+
nextIdxA
nextIdxB
3
pred
pred
indB
indA
Recv (out)
<
m
indB [0:bn]
indA [0:an]
matchedInd[0:N]
Reset
0
=
=
3
pred
pred
indB
indA
Reuse?
Reuse?
Cyclic dependence loop. Low throughput!!

## Slide 9: Feature 3: Data-dependent control in a PE
Function
Unit
Register
File
MUX
MUX
Controller
Memory
Mem. Controller
CLT
MUX
f (inst_out, control_in) → reuse1,reuse2, discard,reset
CLT
CGRA Processing Element
reuse
reset
reuse
discard

## Slide 10: Feature 3: Data-dependent control in a PE
Example LUT config:
if(inp1==INF && inp2==INF) return 3;
if (inp1 == inp2) return 0;
else if (inp1 > inp2) return 1;
else return 2;
Example func unit: Compare
Compare
Register
File
MUX
MUX
CLT
MUX
CGRA Processing Element
reuse
reset
reuse
discard
12
13
INF
14
INF
Self Ctrl i/p | Signal
1 | Reuse1
2 | Reuse2
3 | Reset
Notes: For supporting stream-join in hardware, we add control look-up table which takes the control value as input and applies these are control operations: reuse, reset, and discard. To support reuse, there is support for flow control as well.

## Slide 11: Feature 3: Data-dependent control in a PE
Example LUT config:
if(inp1==INF && inp2==INF) return 3;
if (inp1 == inp2) return 0;
else if (inp1 > inp2) return 1;
else return 2;
Example func unit: Compare
Self Ctrl i/p | Signal
1 | Reuse1
2 | Reuse2
3 | Reset
Compare
Register
File
MUX
MUX
CLT
MUX
CGRA Processing Element
reuse
reset
reuse
discard
12
13
INF
14
INF
POP
NO-POP
2
Notes: For supporting stream-join in hardware, we add control look-up table which takes the control value as input and applies these are control operations: reuse, reset, and discard. To support reuse, there is support for flow control as well.

## Slide 12: Feature 3: Data-dependent control in a PE
Example LUT config:
if(inp1==INF && inp2==INF) return 3;
if (inp1 == inp2) return 0;
else if (inp1 > inp2) return 1;
else return 2;
Example func unit: Compare
Self Ctrl i/p | Signal
1 | Reuse1
2 | Reuse2
3 | Reset
Compare
Register
File
MUX
MUX
CLT
MUX
CGRA Processing Element
reuse
reset
reuse
discard
INF
13
14
INF
NO-POP
POP
1
Notes: For supporting stream-join in hardware, we add control look-up table which takes the control value as input and applies these are control operations: reuse, reset, and discard. To support reuse, there is support for flow control as well.

## Slide 13: Feature 3: Data-dependent control in a PE
Example LUT config:
if(inp1==INF && inp2==INF) return 3;
if (inp1 == inp2) return 0;
else if (inp1 > inp2) return 1;
else return 2;
Example func unit: Compare
Self Ctrl i/p | Signal
1 | Reuse1
2 | Reuse2
3 | Reset
Compare
Register
File
MUX
MUX
CLT
MUX
CGRA Processing Element
reuse
reset
reuse
discard
INF
14
INF
NO-POP
POP
1
Notes: For supporting stream-join in hardware, we add control look-up table which takes the control value as input and applies these are control operations: reuse, reset, and discard. To support reuse, there is support for flow control as well.

## Slide 14: Feature 3: Data-dependent control in a PE
Example LUT config:
if(inp1==INF && inp2==INF) return 3;
if (inp1 == inp2) return 0;
else if (inp1 > inp2) return 1;
else return 2;
Example func unit: Compare
Self Ctrl i/p | Signal
1 | Reuse1
2 | Reuse2
3 | Reset
Compare
Register
File
MUX
MUX
CLT
MUX
CGRA Processing Element
reuse
reset
reuse
discard
INF
INF
POP
POP
3
Reset
Notes: For supporting stream-join in hardware, we add control look-up table which takes the control value as input and applies these are control operations: reuse, reset, and discard. To support reuse, there is support for flow control as well.

## Slide 15: Outline
Background: Decoupled Spatial Architectures​
Decoupled-Spatial Architecture Programming​
Advanced DSA Programming​
  Warm up: Support for data-dependent control/memory
  Exercise 3: Sparse vector-vector dot-product (Hands-on-exercise)
  Full SpMSpV and Multi-core implementation
Compiling High-Level Lang. to DSA​
Composing a Spatial Architecture​

## Slide 16: Hands-on-Exercise: (Find index when index-data matched!!)
// vanilla C code
while (i < an && j < bn):
if (indA[i] == indB[j]):
matchInd[++iout] = indA
++i; ++j
elif (indA < indB):
++i
else:
++j
Recv (done)
<
indA [0:an]
indA [0:an]
m
indA [0:an]
indA [0:an]
indB [0:bn]
indA [0:an]
matchedInd[0:N]
f
Reset
3
=
f
done

## Slide 17: Hands-on-Exercise: (Find index when index-data matched!!)
Step 1: Write the DFG (manual/04_join/join.dfg)
Step 2: Write control code (manual/ 04_join/main.cc)

## Slide 18: Step 1: Append the DFG (manual/04_join/join.dfg)
// 04_join/join.dfg
Input: indA
Input: indB
/* Write Compare operation here (Definition below:)
* if (op1 > op2) out = 1
* else if (op2 > op1) out = 2
* else if (op1 == INF) out = 3
* else out = 1
*/
match = Min64(indA, indB, ctrl=pred{1:b1|d, 2:b2|d})
is_end = ICmpEQ(pred, 3, ctrl=pred{1:d, 2:d})
matchedInd = Keep(match, 1, ctrl=is_end{1:d})
done = Keep(match, is_end)
Output: matchedInd, done
Recv (done)
<
indA [0:an]
indA [0:an]
m
indA [0:an]
indA [0:an]
indB [0:bn]
indA [0:an]
matchedInd[0:N]
f
Reset
3
=
f
done
pred | Signal
0 | --
1 | Reuse1, d
2 | Reuse2, d
3 | --
pred | Signal
0 | --
1 | Reuse1
2 | Reuse2
3 | --
Notes: Input: indAInput: indB # generate predicate whether indices match (0 for match and 3 for end # returns the matched indices
Output: matchedIndOutput: done

## Slide 19: Step 1: Append the DFG (manual/04_join/join.dfg)
// 04_join/join.dfg
Input: indA
Input: indB
pred = Compare64(indA, indB, self={1:b1, 2:b2})
match = Min64(indA, indB, ctrl=pred{1:b1|d, 2:b2|d})
is_end = ICmpEQ(pred, 3, ctrl=pred{1:d, 2:d})
matchedInd = Keep(match, 1, ctrl=is_end{1:d})
done = Keep(match, is_end)
Output: matchedInd, done
Recv (done)
<
indA [0:an]
indA [0:an]
m
indA [0:an]
indA [0:an]
indB [0:bn]
indA [0:an]
matchedInd[0:N]
f
Reset
3
=
f
done
pred | Signal
0 | --
1 | Reuse1, d
2 | Reuse2, d
3 | --
pred | Signal
0 | --
1 | Reuse1
2 | Reuse2
3 | --
Notes: Input: indAInput: indB # generate predicate whether indices match (0 for match and 3 for end # returns the matched indices
Output: matchedIndOutput: done

## Slide 20: Step 2: Append control code (manual/04_join/main.cc)
Recv (done)
<
indA [0:an]
indA [0:an]
m
indA [0:an]
indA [0:an]
indB [0:bn]
indA [0:an]
matchedInd[0:N]
f
Reset
3
=
f
done
Useful intrinsics
// Read data from memory
SS_LINEAR_READ(addr, bytes, port);
// Write constant to the port
SS_CONST(port, data, times);
// Write output data to memory
SS_LINEAR_WRITE(port, bytes, addr);

## Slide 21: Step 2: Append control code (manual/04_join/main.cc)
// 04_join/main.cc
SS_LINEAR_READ(&indA[0], an*8, P_join_indA);
SS_CONST(P_join_indA, sentinel, 1);
SS_LINEAR_READ(&indB[0], bn*8, P_join_indB);
SS_CONST(P_join_indB, sentinel, 1);
SS_LINEAR_WRITE(P_join_matchedInd, &output[0], N*8);
SS_RECV(P_join_done, &done_flag);
SS_RESET();
SS_WAIT_ALL();
indA [0:an]
indB [0:bn]
matchedInd[0:N]
Recv (done)
<
indA [0:an]
indA [0:an]
m
indA [0:an]
indA [0:an]
indB [0:bn]
indA [0:an]
matchedInd[0:N]
f
Reset
3
=
f
done
Notes: // reset all streams when the output is accumulated uint64_t done_flag; SS_RECV(P_join_done, done_flag); SS_RESET(); SS_WAIT_ALL();

## Slide 22: Run it!! ($ ./run.sh main.out) N=4096, DENSITY=0.1
Simulator Time: 0.02005 sec
Cycles: 799
Number of coalesced SPU requests: 0
Control Core Insts Issued: 35
Control Core Discarded Insts Issued: 17
Control Core Discarded Inst Stalls: 0.4857
Control Core Config Stalls: 0
Control Core Wait Stalls:
ACCEL 0 STATS ***
Commands Issued: 5
CGRA Instances: 40 -- Activity Ratio: 0.9787, DFGs / Cycle: 0.05006
For backcgra, Average thoughput of all ports (overall): 0.02503, CGRA outputs/cgra busy cycles: 0.05115
CGRA Insts / Computation Instance: 60.65
CGRA Insts / Cycle: 3.036 (overall activity factor)
Mapped DFG utilization: 0.6073
Index-match is done at a line rate

## Slide 23: Outline
Background: Decoupled Spatial Architectures​
Decoupled-Spatial Architecture Programming​
Advanced DSA Programming​
  Warm up: Support for data-dependent control/memory
  Exercise 3: Sparse vector-vector dot-product (Hands-on-exercise)
  Full SpMSpV and Multi-core implementation
Compiling High-Level Lang. to DSA​
Composing a Spatial Architecture​

## Slide 24: Example 3: SpMSpV (Dot product kernel)
// vanilla code
while (i < an && j < bn):
if (indA[i] == indB[j]):
out += valA[i]* valB[j]
++i; ++j
elif (indA[i] < indB[j]):
++i
else:
++j
Recv (O)
<
indA
[0:an]
matchIndA[0:N]
indB
[0:bn]
x
valA [0:N]
m
cntIndA
[0:an]
cntIndB
[0:an]
indB [0:bn]
indA [0:an]
matchIndB[0:N]
valB [0:N]
+
f
discard
+
+
Indirect access to values at matched indices
counter
Notes: To avoid fragementation, we would move to using offset array instead of cnt for dot product.
Why matched index? That means value array is stored in the dense format?
Also, error to keep a filter?
// join of indices SS_DMA_READ(&matrix_row_ind[row_offset[row]], 0, (row_offset[row+1]-row_offset[row]) * 8, 1, P_dotp_indA); SS_CONST(P_dotp_indA, sentinel, 1); SS_DMA_READ(&vector_ind[0], 0, vec_len * 8, 1, P_dotp_indB); SS_CONST(P_dotp_indB, sentinel, 1); // indirect access to the values of matched indices (unknown length) SS_INDIRECT(P_dotp_matchIndA, &matrix_row_val[row_offset[row]], M, P_dotp_matchValA); SS_INDIRECT(P_dotp_matchIndB, &vector_val[0], M, P_dotp_matchValB); // reset all streams when the output is accumulated SS_RECV(P_dotp_O, output[row]); SS_RESET(); SS_WAIT_ALL();

## Slide 25: Example 3: SpMSpV (manual/05_spmv/) (density=1 N=4096 DT=64)
Simulator Time: 0.2533 sec
Cycles: 4155
ACCEL 0 STATS ***
Commands Issued: 8
CGRA Instances: 8193 -- Activity Ratio: 0.9894, DFGs / Cycle: 1.972
For backcgra, Average thoughput of all ports (overall): 0.6573, CGRA outputs/cgra busy cycles: 1.993
CGRA Insts / Computation Instance: 3.5
CGRA Insts / Cycle: 6.902 (overall activity factor)
Mapped DFG utilization: 0.986

## Slide 26: Example 3: SpMSpV (manual/05_spmv/) (density=0.1 N=4096 DT=64)
Simulator Time: 0.04866 sec
Cycles: 924
ACCEL 0 STATS ***
Commands Issued: 8
CGRA Instances: 87 -- Activity Ratio: 0.8452, DFGs / Cycle: 0.09416
For backcgra, Average thoughput of all ports (overall): 0.03139, CGRA outputs/cgra busy cycles: 0.1114
CGRA Insts / Computation Instance: 37.29
CGRA Insts / Cycle: 3.511 (overall activity factor)
Mapped DFG utilization: 0.5015
Can exploit sparsity at a near-line rate index match

## Slide 27: Example 4: SpMSpV (Parallelizing Dot products across cores)
// vanilla code
int tid = row;
while (row < N):
out_arr[row] = dotp (mat[row], vec)
row += core_cnt
pthread_barrier_wait(&barr);
Main Memory
Global Stream Engine
DSA Core
DSA Core
DSA Core
…
DSA Core
DSA Core
DSA Core
DSA Core
DSA Core
DSA Core
…
…
…
…
…
dotp (matrix[0], vector)
barrier
dotp (matrix[16], vector)
barrier
…
2. Synchronization
1. Core-to-core communication
3. Mapping data to scratchpad space
Notes: while(row<N) { // considering granularity as row row += NUM_THREADS; dotp_impl(row); }

## Slide 28: Multicore Explicit Communication Primitives
SS_REM_PORT(out_port, num_elem, mask, rem_port);
SS_SCRATCH_READ(scr_addr, n_bytes, port)
... and other cmd as DMA
A) Explicit Multicast from a port to masked cores/ports
B) Implicit communication using global address space
Vector ports
Vector ports
Vector ports
Vector ports
Spad
Spad
Spad
Spad
Vector ports
Vector ports
Vector ports
Vector ports
Spad
Spad
Spad
Spad
Core 1
Core 2
Core 3
Core 4
Core 1
Core 2
Core 3
Core 4
Ctrl
Ctrl
Ctrl
Ctrl
Ctrl
Ctrl
Ctrl
Ctrl
Notes: #define SS_WAIT_DF(num_rem_writes, scratch_type) \ __asm __volatile__("ss_wait_df %0, %1" : : "r"(num_rem_writes), "i"(scratch_type));
Multicore primitives
1. Multicast
2. Global barrier: waiting on the specified number of threads
Global address space: (core_id)(local_address)
Current address mapping is linear.
To preprocess graph for locality: Find a mapping function and change vertex id according to that.

## Slide 29: Multicore Synchronization Primitives
SS_WAIT_DF(num_rem_writes, spad_type)
SS_GLOBAL_WAIT(num_threads)
B) Global synchronization for all tasks
A) Barrier until N bytes are written to local spad
Vector ports
Vector ports
Vector ports
Vector ports
Spad
Spad
Spad
Spad
Ctrl
Ctrl
Ctrl
Ctrl
Vector ports
Vector ports
Vector ports
Vector ports
Spad
Spad
Spad
Spad
Ctrl
Ctrl
Ctrl
Ctrl
2+4+3 = 9 total writes
2
3
4
Notes: #define SS_WAIT_DF(num_rem_writes, scratch_type) \ __asm __volatile__("ss_wait_df %0, %1" : : "r"(num_rem_writes), "i"(scratch_type));
Multicore primitives
1. Multicast
2. Global barrier: waiting on the specified number of threads
Global address space: (core_id)(local_address)
Current address mapping is linear.
To preprocess graph for locality: Find a mapping function and change vertex id according to that.

## Slide 30: Multicore Configurable Data Mapping
SS_CFG_MEM_MAP(part_size, active_core_bv, map_type)
DSA Core
DSA Core
DSA Core
…
DSA Core
DSA Core
DSA Core
DSA Core
DSA Core
DSA Core
…
…
…
…
…
Example 2: Subset of cores
Example 1: cyclic
DSA Core
DSA Core
DSA Core
…
DSA Core
DSA Core
DSA Core
DSA Core
DSA Core
DSA Core
…
…
…
…
…
Part_size
Active_core_bv = “1111…”
Active_core_bv = “001100…”
Currently, map_type is default cyclic but we would like to study replication.
Notes: #define SS_CONFIG_MEM_MAP(part_size, active_core_bv, map_type) \ __asm__ __volatile__("ss_cfg_mmap %0, %1, %2" : : "r"(part_size), "r"(active_core_bv), "i"(map_type));

## Slide 31: Example 4: SpMSpV multicore implementation
// manual/07_spmv_multicore/main.cc
if(tid==0) {
SS_DMA_READ(&indA[0], 0, an, 1, P_IND_1);
uint64_t bdcast_mask=pow(2,num_cores)-1;
SS_REM_PORT(P_IND_1, an*8, bdcast_mask, P_dotp_indA);
}
dotp_impl(); // no need to load vector here
SS_GLOBAL_WAIT(16);
Main Memory
Global Stream Engine
DSA Core
DSA Core
DSA Core
…
DSA Core
DSA Core
DSA Core
DSA Core
DSA Core
DSA Core
…
…
…
…
…
Read at core 1 (ie. tid=0) and broadcast to all cores
Notes: }

## Slide 32: Results with Basic pthread Support (num_threads=4 density=0.1 N=8192)
*** ROI STATISTICS for CORE ID: 1 ***
Cycles: 7312
GRA Instances: 647 -- Activity Ratio: 0.4546, DFGs / Cycle: 0.08848
Mapped DFG utilization: 0.25
*** ROI STATISTICS for CORE ID: 2 ***
Cycles: 7328
CGRA Instances: 661 -- Activity Ratio: 0.4615, DFGs / Cycle: 0.0902
Mapped DFG utilization: 0.2493
*** ROI STATISTICS for CORE ID: 4 ***
Cycles: 7286
CGRA Instances: 641 -- Activity Ratio: 0.4547, DFGs / Cycle: 0.08798
Mapped DFG utilization: 0.251
*** ROI STATISTICS for CORE ID: 3 ***
Cycles: 7346
CGRA Instances: 635 -- Activity Ratio: 0.4597, DFGs / Cycle: 0.08644
Mapped DFG utilization: 0.249
Lower DFG utilization due to network traffic (25% vs 45% for a single core)

## Slide 33: Results: manual/07_spmv_multicore/ (num_threads=4 density=0.1 N=8192)
*** ROI STATISTICS for CORE ID: 1 ***
Cycles: 5316
CGRA Instances: 647 -- Activity Ratio: 0.585, DFGs / Cycle: 0.1217
Mapped DFG utilization: 0.3439
*** ROI STATISTICS for CORE ID: 2 ***
Cycles: 5384
CGRA Instances: 661 -- Activity Ratio: 0.5914, DFGs / Cycle: 0.1228
Mapped DFG utilization: 0.3393
*** ROI STATISTICS for CORE ID: 4 ***
Cycles: 5286
CGRA Instances: 641 -- Activity Ratio: 0.6035, DFGs / Cycle: 0.1213
Mapped DFG utilization: 0.3459
*** ROI STATISTICS for CORE ID: 3 ***
Cycles: 5281
CGRA Instances: 635 -- Activity Ratio: 0.6095, DFGs / Cycle: 0.1202
Mapped DFG utilization: 0.3463
DFG utilization improves with multicast (34% vs 25%)

## Slide 34: BACKUP

## Slide 35: Example 3: SpMV (Dot product kernel)
// 05_spmv/merge.dfg
Input: indA, indB, matchValA, matchValB
pred = Compare64(indA, indB, self={1:b1, 2:b2})
cntIndA = Acc64(1, 0, ctrl=pred{1:a})
cntIndB = Acc64(1, 0, ctrl=pred{2:a})
matchInd = Min64(cntIndA, cntIndB, ctrl=pred{1:b1|d, 2:b2|d, 3:d})
mult = Mul64(matchValA, matchValB)
done = Keep(pred, 1, ctrl=pred{1:d,2:d})
O = Acc64(mult, ctrl=done{0:d,3:r})
Output: matchIndA, matchIndB, O
Recv (out)
Recv (O)
<
indA
[0:an]
matchIndA[0:N]
indB
[0:bn]
x
valA [0:N]
m
cntIndA
[0:an]
cntIndB
[0:an]
indB [0:bn]
indA [0:an]
matchIndB[0:N]
valB [0:N]
+
f
discard
+
+
Notes: To avoid fragementation, we would move to using offset array instead of cnt for dot product.
Why matched index? That means value array is stored in the dense format?
Also, error to keep a filter?

## Slide 36: Example 3: SpMV (Dot product kernel)
// 05_spmv/main.cc
SS_LINEAR_READ(indA, an*8, P_dotp_indA);
SS_CONST(P_dotp_indA, sentinel, 1);
SS_LINEAR_READ(indB, bn* 8, P_dotp_indB);
SS_CONST(P_dotp_indB, sentinel, 1);
SS_INDIRECT(P_dotp_matchIndA, valA, N, P_dotp_valA);
SS_INDIRECT(P_dotp_matchIndB, valB, N, P_dotp_valB);
SS_RECV(P_dotp_O, output[row]);
SS_RESET();
SS_WAIT_ALL();
Recv (O)
<
indA
[0:an]
matchIndA[0:N]
indB
[0:bn]
x
valA [0:N]
m
cntIndA
[0:an]
cntIndB
[0:an]
indB [0:bn]
indA [0:an]
matchIndB[0:N]
valB [0:N]
+
f
discard
+
+
Notes: To avoid fragementation, we would move to using offset array instead of cnt for dot product.
Why matched index? That means value array is stored in the dense format?
Also, error to keep a filter?
// join of indices SS_DMA_READ(&matrix_row_ind[row_offset[row]], 0, (row_offset[row+1]-row_offset[row]) * 8, 1, P_dotp_indA); SS_CONST(P_dotp_indA, sentinel, 1); SS_DMA_READ(&vector_ind[0], 0, vec_len * 8, 1, P_dotp_indB); SS_CONST(P_dotp_indB, sentinel, 1); // indirect access to the values of matched indices (unknown length) SS_INDIRECT(P_dotp_matchIndA, &matrix_row_val[row_offset[row]], M, P_dotp_matchValA); SS_INDIRECT(P_dotp_matchIndB, &vector_val[0], M, P_dotp_matchValB); // reset all streams when the output is accumulated SS_RECV(P_dotp_O, output[row]); SS_RESET(); SS_WAIT_ALL();

## Slide 37: Example 2: SpMV ($ ./run.sh main.out DENSITY=0.1 N=4096 DT=64)
Simulator Time: 2.59 sec
Cycles: 95651
ACCEL 0 STATS ***
Commands Issued: 512
CGRA Instances: 5276 -- Activity Ratio: 0.543, DFGs / Cycle: 0.05516
For backcgra, Average thoughput of all ports (overall): 0.01839, CGRA outputs/cgra busy cycles: 0.1016
CGRA Insts / Computation Instance: 39.38
CGRA Insts / Cycle: 2.172 (overall activity factor)
Mapped DFG utilization: 0.3103
Matrix occupies more space, needs double buffer for better hit rate

## Slide 38: Example 2: Dot product ($./run.sh main.out DENSITY=0.1 N=1024 DT=16)
Simulator Time: 0.04666 sec
Cycles: 225
Number of coalesced SPU requests: 0
Control Core Insts Issued: 53
Control Core Discarded Insts Issued: 18
Control Core Discarded Inst Stalls: 0.3396
Control Core Config Stalls: 0.04889
Control Core Wait Stalls:
ACCEL 0 STATS ***
Commands Issued: 8
CGRA Instances: 5 -- Activity Ratio: 0.9244, DFGs / Cycle: 0.02222
For backcgra, Average thoughput of all ports (overall): 0.007407, CGRA outputs/cgra busy cycles: 0.02404
CGRA Insts / Computation Instance: 165.8
CGRA Insts / Cycle: 3.684 (overall activity factor)
Mapped DFG utilization: 0.5263
Pipelined execution of smaller data-width vectors

## Slide 39
Main Memory
Global Stream Engine
SPU Core
SPU Core
SPU Core
…
SPU Core
SPU Core
SPU Core
SPU Core
SPU Core
SPU Core
…
…
…
…
…
Useful Communication Patterns
Main Memory
Global Stream Engine
SPU Core
SPU Core
SPU Core
…
SPU Core
SPU Core
SPU Core
SPU Core
SPU Core
SPU Core
…
…
…
…
…
Main Memory
Global Stream Engine
SPU Core
SPU Core
SPU Core
…
SPU Core
SPU Core
SPU Core
SPU Core
SPU Core
SPU Core
…
…
…
…
…
Fully Connected Layer
(broadcast row)
  Sparse Convolution
  (communication with neighbors for halos)
Independent Lanes
(with/without Communication)
Local Spatial Communication
Pipelined Communication
  Arithmetic Circuits – Pipelined DAG Traveral
  (pipeline node updates)
Graph Processing
(core-core communication)

## Slide 40: Feature 2: Data-dependent length
SS_RECV(port, mem_addr)
Port A
mem_addr
Acts as a barrier until a value from a port is written to a memory location
SS_RESET()
Memory
Controller
Stream table
Stream 0
Stream 1
…
Stream N
Resets all pending read requests and active streams except live data
Pending memory reqs
Notes: SS_RESET()
for existing read streams: drops pending requests and sets num_elem to 0
For existing write streams: sets num_elem to 0 when the vector_port is empty
/*! * \brief Drop all the ongoing data request while retaining the configuration. */#define SS_RESET() \ __asm__ __volatile__("ss_cfg x0, 0") /*! * \brief Reset all live streams after finishing all ports */#define SS_STREAM_RESET() \ __asm__ __volatile__("ss_cfg x0, 1");

## Slide 41: Features to Support Data-dependence
Data-dependent memory access
  Specifying Dependent memory streams
Managing data-dependent length
  Identifying and dynamically broadcasting done signal
Data-dependent control in processing element:
  Configurable Control Lookup Table (CLT) for PEs